## Slide 1: Aviation safety & certification of new operations and systems
WP3 – Safety Risk Management
User Group Meeting #2
19 & 20th September, 2013 at JRC
Prepared by Jean-Pierre MAGNY, Alfred ROELEN, Izaro Etxebarria Güena, Heiko UDLUFT, Véronique BONVINO
Presented by Jean-Pierre HECKMANN

## Slide 2: Agenda
Thursday 19th September - Results of Work Package 3
13:30-13:45 WP3.1 Results of D3.1 - Total Aviation Safety Assessment Methodology
13:45-14:00 WP3.1 Questions/discussion/feedback on D3.1 with User Group members
14:00-14:15 WP3.2 Results of D3.2 - Risk models and accident scenarios
14:15-14:30 WP3.2 Questions/discussion/feedback on D3.2 with User Group members

## Slide 3
WP3.1 Total Aviation Safety Assessment Methodology

## Slide 4: Total Aviation Safety Assessment Methodology (1/6)
Needs and criteria for a total aviation system safety method
Overview of needs | 
A. | The method has to address Total Aviation System and to provide the means to address all interfaces and interactions between different aviation system domains
B. | The method should make use of more integrated supporting tools for safety assessment
C. | The method has to address current and future risks
D. | The method has to be appropriate for supporting the certification process from WP1
E. | The method has to address all lifecycle phases
F. | The method has to be appropriate for developing safety assessments of good quality
G. | The method has to make use of inputs from experts with appropriate qualifications
H. | The method should adopt stakeholders’ wishes

## Slide 5: Introduction to FAST and the concept of Area of Change
  Future Aviation Safety Team (FAST): multi-disciplinary, international safety experts that identifies and publishes emerging and future risks across aviation and space sectors
  FAST repository of Areas of Change (AoC) is regularly re-audited by the FAST Team
        AoC : any phenomenon that will affect aviation safety either from within aviation system or from external domains
  FAST provides a Risk Picture of the future to all actors during the entire life cycle
  FAST provides indications where to searching for precursors
  FAST recommends using AoCs also to enrich analysis/efficacy of risk control measures
        Already done with Joint Implementation Measurement Data Analysis Team (JIMDAT) for 14 safety enhancements
  ASCOS has updated and improved an existing list of emerging risks from FAST
  The FAST process is not a risk assessment method, it doesn’t estimate relative frequency of hazards. It’s augmenting, not replacing existing activities. FAST generally does not recommend or develop safety interventions left to Risk Assessment & Risk Management
10 years ago FAST had identified emerging risks associated to major changes and events scenarios leading to recent accidents.  AF 447, JK 5022, TK 1509, ASIANA 214
Total Aviation Safety Assessment Methodology (2/6)

## Slide 6: Total Aviation Safety Assessment Methodology (3/6)
Process for identification of precursors for future and emerging risks
ASCOS improves precursors detection efficacy
  Use development (safety barriers, lines of defense) whose degradations are precursors.
  Identify Events Sequences Diagrams permitting to place any event in these diagrams
    Synergy between CATS  FAST  Organization  certification & lessons learned
  Establish links between the development logic, its ability to provide validation results, (e.g. sensitivity analysis) usable for operational phases  certification & lessons learned
    Achievable through developers / operators improved cross fertilization (organization)
  Further develop root causes analysis in order to place incidents at the level of deeper roots and spread out precursors identification at that level
  Complete accident reports analysis accordingly (beyond investigation boards mandate)

## Slide 7
Total Aviation Safety Assessment Methodology (4/6)
Causal Model of Air Transport Safety – CATS
Objective: The prevention of aircraft accidents through better understanding of aviation risks in terms of causes and magnitude.
CATS is a risk analyses tool to support decision making in safety management
Describes total aviation system
33 accident scenario’s with underlying causes
Representation by event sequence diagrams and fault trees
Human Performance Models (Flight crew, ATC, Maintenance)
Generic consequence model (fatalities and aircraft damage)
CATS was developed for the Dutch Ministry of Infrastructure and the Environment

## Slide 8
Total Aviation Safety Assessment Methodology (5/6)
Why FAST & CATS have been selected as basis for a method
By using CATS & FAST, the most important identified needs and criteria are met
CATS and FAST cover the total aviation system, including all the aviation domains
CATS quantifies all current risks in the total aviation system (baseline risk picture), and is used by authorities (e.g. CAA NL, FAA) as a valid method to quantify aviation safety
FAST is recognised by EASA and FAA as promising approach to establish a method for assessing future risks of an appropriately scoped future system in its future context
Methods can be introduced in design, development, operations (all life cycle phases)
CATS and FAST can be easily embedded in the outline certification process from WP1
Early involvement of stakeholders and well qualified experts is easy to realise/achieve

## Slide 9: Total Aviation Safety Assessment Methodology (6/6)
Overall conclusions and recommendations – Results
Methodologies
Identified methods should be published as part of safety training material decision makers
Fields of application and management
Promote more safety effort in early program phases,
  Taking care of future risk picture (engineering + safety)
  Maturity demonstrations of new technologies start with early program phases
  Complexity of organizations taken care of in Management methods & standards
Certification considerations
  Certification, considered as a product from design justifications (from concept)
  Updated design justification have to replace older possibly obsolete regulations
Precursors
  Precursors detection methods continuity between development and operations
  Precursors detection methods have to become a standard or at least a handbook
Air/ground interfaces (e.g. NextGen and SESAR)
  For a tight integration of engineering and safety assessment practices on both sides it looks necessary to set up a central engineering coordination unit (e.g. Ariane,)
Standardization shall recommend systematic application and insertion in Safety Plans
  Standards like ARP4754 rev A recommend development practices. The dependency of Safety on program management matters votes for going further that way .

## Slide 10: Total Aviation Safety Assessment Methodology Questions
Topics for questions
  Methodologies
  Fields of application and management
  Certification considerations
  Precursors
  Air/ground interfaces (e.g. NextGen and SESAR)
  Standardisation

## Slide 11
WP3.2 Risk models
and Accident Scenarios

## Slide 12
The aims of the ASCOS WP3.2 are to provide an integrated approach of risk modeling in which human factors and cultural aspects are considered. This work comprises four sub tasks:
  Representation of the current aviation system in accident scenarios using CATS and introducing accident precursor concept
  Representation of emerging and future risks in accident scenarios using experience of the future Aviation Safety team (FAST)
  Representation of the safety management and safety management culture in accident scenarios
Risk model and accident scenarios: Results presentation
Risk models and accident scenarios (1/7)

## Slide 13: Risk models and accident scenarios (2/7)
Representation of the current aviation system in accident scenarios – Results:
  ASCOS model based on CATS
  29 accident scenarios represented as ESDs
  Events are further detailed in Fault Trees

## Slide 14: Risk models and accident scenarios (3/7)
Safety barrier: take off failure detection (conditional)
Example: simplified runway excursion/over-run at take off with Initiating event “Aircraft system failure”
Aircraft System failure other than directional control system and engine
Take off failure detection (conditional)
Flight crew rejects take off
V>V1
Over run
Continue take off
Yes
No
1
2
3
1
2
3
Safety barrier:
aircraft system integrity
fault tree for “aircraft system failure”
Fault tree for failure of “warning inhibition” at take off
Safety barrier:
- Stop and go procedure
- Rejected take off procedure
fault Tree for “take off rejection decision and procedure “ failure
6
Fail to achieve maximum braking
Brakes failure
Brakes not applied correctly
Brakes too hot
Poor Runway maintenance for rubber deposit removal
6
Safety barrier:
Achieve max. braking
Fault Tree for “Fail to achieve max. braking”
Insufficient runway length
Fault tree associated to failure of safety barrier “Achieve max braking”
Failure to achieve max braking
Over run
Stop on runway
6
Continue take off
Safety barrier:
Achieve max. braking

## Slide 15: Risk models and accident scenarios (4/7)
Representation of future risks in risks models – Results:
Precursor linked to base events of fault trees
Application of precursor capture process and calculating precursor occurrence rates.
Precursor = identifiable event that may be used as early warning for known or potential hazards

## Slide 16: Risk models and accident scenarios (5/7)
Representation of safety culture and safety management – Results:
Safety culture and safety management cannot be explicitly represented in the risk model:
Active failures vs latent failures
Common cause influences
Difficult to measure

## Slide 17: Risk models and accident scenarios (6/7)
Use of the risk model to support safety and quantification of accident scenarios – Results:
Process for quantification described
Updated probabilities for the model provided in WP 2.2

## Slide 18: Risk models and accident scenarios (7/7)
Overall conclusions and recommendations : Results:
Updated risk model
Process for representation of future risks

## Slide 19: Risk models and accident scenarios (1/5)
Representation of the current aviation system in accident scenarios – Questions:
Is the level of detail of the risk model appropriate for application of the model in the context of certification?

## Slide 20: Risk models and accident scenarios (2/5)
Representation of future risks in risks models – Questions:
Do we need to develop this part of the model for each new certification question, or is there need for a ‘universally applicable’ list of precursors and links with the model?

## Slide 21: Risk models and accident scenarios (3/5)
Representation of safety culture and safety management – Questions:
Is the proposed “modification factor” for representation of safety culture and safety management sufficient and acceptable?

## Slide 22: Risk models and accident scenarios (4/5)
Quantification of accident scenarios – Questions:
How do we determine that the quantification is correct?

## Slide 23: Risk models and accident scenarios (5/5)
Overall conclusions and recommendations : Questions:
How can a risk model be applied in certification?

## Slide 24
The reproduction, distribution and utilization of this document as well as the communication of its contents to others without express authorization is prohibited. Offenders will be held liable for the payment of damages. All rights reserved in the event of the grant of a patent, utility model or design.
Thank you for your attention!

## Slide 25: Agenda
Friday 20th September -Future Work in Work Package 3
Goals: To present very briefly the scope of the future work in WP3 with a focus on the following on-going deliverables and to obtain input from the User Group relevant for the future work.
13:00-13:15 WP3.3 - Tools for risk assessment and user manual brief presentation
13:15-13:30 Questions/discussion/feedback on W3.3 content with User Group members
13:30-13:45 WP3.4 Overall safety impact results and user manual presentation
13:45-14:00 Questions/discussion/feedback on W3.4 content with User Group members
13:30-13:45 WP3.5 Total aviation system safety standards
13:45-14:00 Questions/discussion/feedback on W3.5 content with User Group members

## Slide 26
WP3.3 Tool for Risk Assessment

## Slide 27: Tool for risk assessment (1/5)
Objectives of work package 3.3
Build a prototype tool to support risk assessment
Tasks according to DoW
  Software requirements definition
  Software functional design
  Code development
  Code verification
  User manual development
  Familiarization workshop organization

## Slide 28: Tool for risk assessment (2/5)
Main functionalities
Support risk assessment for a proposed change (within scope of ASCOS)
Incorporate model developed in WP3.2
Provide guidance/training for inexperienced users

## Slide 29: Tool for risk assessment (3/5)
Architecture / data
Different software architectures being evaluated
  Web-based solution
  Stand-alone software
  MS Office based tool
User will input data to WP3.2 model
  I.e. update CATS element probabilities
  Allow uncertainty
  Model validity needs to be ensured

## Slide 30: Tool for risk assessment (4/5)
High-level functional flow
Identify elements affected by proposed change
Update elements in model
Output results (resulting probabilities)
Validity check

## Slide 31: Tool for risk assessment (5/5)
Supporting documents / workshops
User manual
  Complete description of software functionality
  Explanation of underlying methodology
Online help in software
  Support user while using software
Wizard
  Step-by-step workflow using the software
Course in e-learning environment
Familiarization workshop
  Introduce software to users
  Possibly utilize example cases

## Slide 32: Tool for risk assessment - Questions (1/5)
Current risk assessment practice?
How do you currently perform risk assessment?
  Team size?
  Collaboration partners?
  Sharing of information/information management?
What tools are used currently?
  Which functions of these tools do you like?
  Which functions do you miss from these tools?

## Slide 33: Tool for risk assessment- - Questions (2/5)
ASCOS risk assessment tool requirements?
What do you expect from the ASCOS risk assessment tool
  Name one functionality a risk assessment tool needs to provide?
  What information would be useful to support you in doing risk assessment?
  In what format (ie. report/graphic/table) would you prefer output?
Whom do you need to share information/data with?
  Coworkers?
  Project partners?
  Other stakeholders?

## Slide 34: Tool for risk assessment - Questions (3/5)
Human machine interface?
Do you have a platform preference/experience?
  Web-based
  Stand alone software
  MS Office based tool
How do you prefer to interact with software
  Guided step-by-step wizard
    Rigid structure
    little previous training required
  Direct manual data input/modification in model
    Offers more flexibility and control
    Previous training required

## Slide 35: Tool for risk assessment- Questions (4/5)
Input from user group ?
Currently Software would be reviewed after completion
Would you be interested/available to give feedback during the software development phase?
  Feedback on planned functionality
  Test early software version
  Review user manual

## Slide 36: Tool for risk assessment - Questions (5/5)
Any other feedback?

## Slide 37
WP3.4 Tool for Overall Safety Impact
19-20 th SEPT, 2013

## Slide 38: PLAN
Introduction;
Task objectives;
The approach;
Activities to be performed (sub-tasks);
  On going activities;
Reference to the 1st UG meeting.
Tool for Overall Safety Impact (1/10)

## Slide 39: WP3.4 TOOL FOR OVERALL SAFETY IMPACT
Introduction
One of the challenges for safety of future ATM is to cope with traffic density and complexity;
Air Traffic Controllers will be facing more complex traffic and will be hence subjected to greater workload;
Safety evaluation is linked to the level of air transport network complexity and stability: increases of complexity will lead to lower safety levels.
Tool for Overall Safety Impact (2/10)

## Slide 40
Task Objective:
(source: Description of Work (DoW))
To model a macroscopic scenario for network-wide safety analysis;
The network wide safety analysis is based on identifying safety critical points and safety benefits that can arise out of foreseen changes in the Total Aviation System;
Tool for Overall Safety Impact (3/10)
WP3.4 TOOL FOR OVERALL SAFETY IMPACT

## Slide 41: Approach- The tool
ATM-NEMMO tool models the European Air Transportation network;
From a traffic sample the tool creates a dynamic graph composed of nodes and edges (Complexity Theory) where the nodes are representing the airports and edges are aircrafts flying from one airport to another.
Airports
Aircraft- Flight connecting two airports
Tool for Overall Safety Impact (4/10)

## Slide 42: Approach- The tool
Monitoring Performance Indicators
These indicators will be used to assess the safety implications that could arise when implementing new changes in the total aviation system
Indicator
Average values of the PI per hour
Tool for Overall Safety Impact (5/10)

## Slide 43
Activities to be performed (sub-Tasks)
Define the modeling Scenario, considering foreseen changes in the Total Aviation System;
Define the Performance Indicators (PI)/ metrics that will be calculated to support the analysis: they will be a priori, related to Predictability-Efficiency Key Performance Areas (KPA).
Tool for Overall Safety Impact (6/10)

## Slide 44
Activities to be performed (sub-Tasks)
Define Simulation Exercise Plan: a set of exercises will be conducted (Monte Carlo simulation).
Analysis of the simulation results and overall safety impact assessment.
Develop a guidance material on how to interpret simulation results to support safety assessment.
Tool for Overall Safety Impact (7/10)

## Slide 45: D3.4 ‘Overall safety impact results and guidance material’
General structure
  Introduction;
  Operational context;
  Simulation Scenarios
  Assumptions and Simplifications;
  List of Indicators and/or metrics;
  Exercise Plan;
  Results Analysis;
  Conclusions on Overall Safety Impact;
  Annex. Guidance material on how to use the results provided but the tool to support safety assessment (Input for WP4.5 Evaluation of Results)
Tool for Overall Safety Impact (8/10)

## Slide 46
Progress made so far/ on going activities
ATM NEMMO tool adaptation works to model the ‘current scenario’:
  Main characteristics are extracted from SESAR documentation.
Draft list of an initial set of Performance Indicators to be calculated by the tool
Tool for Overall Safety Impact (9/10)

## Slide 47
From previous UG meeting:
(Source: User Group 1 Minutes of meeting)
WP3 expectations : Safety Risk Management - Jean Pierre Heckmann, Matthieu Feuvrier (APSYS)
‘…This work package is supposed to include future risks not present in current aviation systems. How far into the future do you want to look? Are you accounting for changes that projects such as SESAR/NextGen will bring?...
Further remarks:
It is important to consider throughout the entire project what the effect of new technologies or new operational procedures may have and how to take this into account. ..’
WP3.4 is considering the operational changes proposed by SESAR for characterizing the reference modelling scenario;
Tool for Overall Safety Impact (10/10)

## Slide 48
WP3.5 Total aviation system safety standards

## Slide 49: WP3.5 Total Aviation System Safety Standards -
The aim of ASCOS WP 3.5 is to develop a process to improve the total aviation system safety standards using lessons learned from experience
ASCOS WP 3.5 uses the results of WP3.1 and 3.2 as well as the outputs of WP1 and WP2 to propose a safety process based on:
  Proposing a safety standards model (document tree) for total aviation system
  Developing principles for development and service event collection for lessons learned (identification of a precursors list to look at and development of precursor collection process)
  Application of precursors collection processes during development and in service phases
  Identifying root causes and deriving lessons learned recommendations
  Formalizing lessons learned recommendations into requirements for design, training, operations, etc. (LLR: Lessons Learned Requirements)
  Identifying and proposing improvement of impacted safety standards and certification documents for LLR application and LLR verification of application.

## Slide 50: Certification related documentation improvement process
Certification related applicable documentation for development of systems
System developments process and certification phases
Development and In service phases
During development and In service safety monitoring applicable documentation
Root cause analysis, Lessons learned and recommendations to include in certification related documents for future programs
events collection and analysis for airworthiness monitoring
lessons learned process applicable documentation
Development of mitigation strategies and implementation on product during development and service phases
WP3.5 Total Aviation System Safety Standards -

## Slide 51
Relations between ASCOS and in service safety monitoring standards
For Aircraft system, recommended practices for in service monitoring are standardized in ARP 5150 document.
The preliminary results of ASCOS and particularly the results of WP3.2 on relation between accident precursors and safety barrier failures can be easily plugged into the ARP 5150 generic in service monitoring process and can be used to improve the practices described in this document
WP3.5 Total Aviation System Safety Standards

## Slide 52: WP3.5 Total Aviation System Safety Standards -
ARP 5150 FIGURE 1 - Overview of the Ongoing Safety Assessment Process
Representation of safety barriers in CATS Event Sequence Diagram (ESD)
Define precursor events to look at from CATS Fault tree “base events”.
List of design and operational safety barriers for a Risk Domain (e.g. runway excursion)
captured precursors events
Deployment of precursor capture processes
CATS ESD Fault Trees and base event
Define capture processes for precursors (during development and in service phases)
- Feed back process on in service aircraft
- Feed back process on documentation used for certification (lessons learned Requirements: LLR)
When a safety risk is recognized as not acceptable, root causes associated to precursor events need to be identified, as well as the recommended mitigation means to apply during certification process of new product(implemented in the documentation used for certification)
assessment of safety risk using CATS ESD
Establish Monitor Parameters
1
Monitor For Events
2
Assess Event and Risks
3
Develop Action Plan
4
Disposition Action Plan
5
ASCOS results from WP 3.1 and 3.2
Correspondence between ARP 5150 process (“Safety Assessment of Transport Airplanes in Commercial Service”) and ASCOS process
CATS ESD Fault Trees and base event
Improvement of certification related documentation for system developments (e.g. Validation/Verification plan/process, Review safety question list, method documents for safety assessments, Safety plan and safety Master Document, instruction and operational documentation
Closing the loop for certification documentation improvement

## Slide 53
Relations between ASCOS and system development standards
To improve the certification related documentation it is necessary to identify the certification related referential used for system development.
The results from ASCOS WP1 and WP 3.1 is that there is no common standards for the development of the different parts of the total aviation system. It is then necessary to develop one common frame in order to assure coherency in the development of the different part of the total aviation system. Having a common development process that can be used for the development of each part of the total aviation system.
ASCOS WP 3.5 will recommend a development model based on the principles of the ARP 4754A and amended as necessary with SESAR results to make it applicable to the development of each part of the total aviation system.
The starting point will be the development process described in the ARP 4754A that is:
    the result of international committees (SAE/EUROCAE),
    recommended by airworthiness authorities (EASA/FAA)
    used by all the aircraft manufacturers
    generic enough to be adapted to the different part of the total aviation system
In this model there will be room for method and tool adaptation to satisfy the specificities of each part of the total aviation system (i.e. use of SESAR results for ATM)
WP3.5 Total Aviation System Safety Standards -

## Slide 54
WP3.5 Total Aviation System Safety Standards -
Intended
Function
System
Design
Information
Functional
System
Function
,
Failure
&
Safety
Information
Guidelines for development of
Total aviation System
(i.e. ARP4754A/ED79A, AIR6218 for aircraft)
Hardware Development
Life
-
Cycle
(
DO
-
254
/
ED
-
80
)
Safety Assessment of Total aviation
In Commercial Service
i.e. ARP5150 for aircraft
Operation
Guidelines for Integrated
Modular Avionics
(
DO
-
297
/
ED
-
124
)
Development Phase
-
In Service Operational Phase
Software Development
Life
-
Cycle
(
DO
-
178
B
/
ED
-
12
B
)
Safety Assessment Process for total aviation system . Guidelines and methods
(i.e. ARP4761/ED135 for aircraft)
REGULATION
Aircraft (i.e. EASA CS25 1309, FAA FAR 25 1309
ATM (1035/2011 annex 2)
Airport?
Operation?
ED = Eurocae Document
DO = DOcument
ARP = Aerospace Recommended Practices
Guidelines Documents for total aviation development process
Starting point for a Safety standards model (document tree) for total aviation system (derived from ARP 4754A)

## Slide 55
Relations between ASCOS and system development standards
ARP 4754A development process is focused on a planning activity and on 8 integral processes that are generic for any industrial development :
    1- Safety assessment
    2- Development assurance level assignment
    3- Requirement capture
    4- Requirement validation
    5- Requirement implementation
    6- Configuration management
    7- Process assurance
    8- Certification and regulatory authority coordination
In addition AIR 6218 gives recommendations for “Constructing Development Assurance Plan For Integrated Systems”
WP3.5 Total Aviation System Safety Standards

## Slide 56: ARP 4754A Aircraft or System Development Process Model
Development process of each part of the total aviation system should apply the following « Integral Processes » that are generic to each industrial development activity (from ARP 4754A)
Each integral process should be structured by:
  - A plan describing, in accordance with development plan, the organization, the responsibilities, the tasks to perform, the management principles, the deliverables. - Method documents describing how to perform tasks identified in the plan and defining deliverables format and contents, - Technical deliverables resulting from the application of the plan and method documents
WP3.5 Total Aviation System Safety Standards
Notes: Figure 4‑2 provides a graphical representation of the system development process model with the numerical entries in each activity box representing the section numbers of this document in which the activity is further explained.

## Slide 57: Certification related Safety documents for Aircraft
High level requirements (Regulation)
Application of ARP 4754A, AIR6218 and ARP 4761 for system development. Application of ARP5150 for airworthiness monitoring
System development Recommended practices
ARP 4754A: Guidance for Development, Validation and Verification of aircraft systems
AIR 6218: Constructing Development Assurance Plan For Integrated Systems
ARP 4761: Guidelines and methods for conducting the safety assessment process of civil airborne systems (and equipment)
CS25
CRI,
Cert Memo
Safety plan,
Validation plan,
Verification plan
Safety Master Document
Lessons learned from experience consideration
Safety review check lists
Safety methods for FHA,PASA, PSSA, SSA, ASA, CMA, HEA, PRA, ZSA, IHA, Safety Synthesis, Safety Review organization
Integrated system specific studies (from AIR 6218)
Item development recommended practices
DO 178 (software items)
DO 254 (Electronic hardware items)
DO 297 (integrated modular avionic)
SOI Reviews
In service safety monitoring
ARP 5150 (Safety assessment of transport airplane in commercial service
In service safety monitoring plan
Method for in service monitoring
Method for deriving and applying lessons learned from development and from in service experiences.
Lessons learned Requirements from experience
Regulation and recommended practices applicable documents for system developments
Certification related documents that can be easily improved (short mid term loop) with lessons learned from experience
SOI (Stage Of Involvement) reviews check lists (planning review, development review, verification review, final review)
Details of certification related documents from application of the ARP 4754A to Aircraft development
WP3.5 Total Aviation System Safety Standards

## Slide 58: LESSONS LEARNED PROCESS (FROM ARP 5150)
WP3.5 Total Aviation System Safety Standards - User Group Meeting – 19th of September, 2013
EXPERIENCE DATA SOURCES
Product support
Continuous airworthiness safety assessment process
Continuous improvement assessment process
Modification process
SUB-PROCESS A: Data selection
SUB-PROCESS C: Elaboration of guidelines, standards, design requirements for future programs
Record results of validation meeting
Elaboration of guidelines, standards, educational courses and design requirements
SUB-PROCESS B: root cause identification and recommendations for current programs
Validation of proposed guidelines, standards, educational courses and design requirements
Prioritization and recording of significant events
DATA SELECTION
AIRCRAFT
IN SERVICE
Recommended action implementation on existing programs
Validation of recommended actions (validation meeting)
Problem identification, analysis of generic causes and recommended action proposal (lessons records)
Record results of validation meeting
Management approval meeting
Management approval meeting
FUTURE PROGRAM:
APPLICATION DURING DESIGN
IMPLEMENTATION OF guidelines, standards, educational courses and design requirements application process
Verification of implementation and application
NOTE:
Traceability between data bases must be kept
NEW DESIGNED AIRCRAFT

## Slide 59
ASCOS WP3.5 preliminary Table of content
Introduction
References
3 Safety standard/ certification documentation referential
  3.1 Applicable safety standards and certification documentation for system development
  3.2 ASCOS Recommended Safety standards and certification document referential
4 Precursor consideration and event collection for lessons learned
  4.1 General concept
  4.2 Risk and precursor definition
  4.3 Accident precursor in the global aviation risk picture (CATS)
  4.4 Accident precursor identification for emerging risk
5 Accident precursor identification during system development phase
  5.1 System architecture main drivers
  5.2 Safety barrier concept
  5.3 Use of safety barrier and precursor concept in safety assessments
  5.4 Integration of safety assessment Failure conditions in CATS risk picture
  5.5 Use of precursor concept for “in service continuous monitoring”
  5.6 Principles for an in service automatic coding of accident precursors
  5.7 Precursor identification following in service accidents
accident precursor collection during development and in service phases
7 Method for total aviation safety standards improvement
  7.1 Method to derive recommendations for safety Risk mitigation
  7.2 Application of recommendations for Safety Risk Mitigation
  7.3 Improvement in precursor collection system
8 Future Risk consideration ( linked with future novelties implementation)
9 Interface with OACI SMS implementation
10 Conclusion
WP3.5 Total Aviation System Safety Standards -

## Slide 60
The reproduction, distribution and utilization of this document as well as the communication of its contents to others without express authorization is prohibited. Offenders will be held liable for the payment of damages. All rights reserved in the event of the grant of a patent, utility model or design.
Thank you for your attention!
Questions?

## Slide 61
The reproduction, distribution and utilization of this document as well as the communication of its contents to others without express authorization is prohibited. Offenders will be held liable for the payment of damages. All rights reserved in the event of the grant of a patent, utility model or design.
Thank you for your attention!

## Slide 62
Aviation Safety and Certification of new Operations and Systems

## Slide 63: WP3 - Safety Risk Management (3/3)
Source: GA Annex I – Figure 1.
2*
WP2
WP1
WP5
WP4
Safety Risk Management
WP3
1*: Regulation and Certification applicable documentary Basis
2*: Safety Performance Indicators (SPI) and baseline Risk Picture
WP6
DRAFT

## Slide 64: Interactions between WP1, WP2, WP3 and WP 4
Input from WP 2: Safety Performance Indicators (SPI) and baseline risk picture
Input from WP 1: Regulations and certification processes for the total aviation system Applicable documentation for Aircraft, ATM, Airport, etc
WP 3.4 (Dec 2013)
Tool for Overall Safety Impact of new safety enhancement on systems or operations
WP 3.1 (June 2013)
Update/Improve of area of change for Identification of potential accident predictive scenarios models and safety barriers
WP 3.2 (June 2013)
Update/Improve accident event sequences and elaboration of accident models to identify safety barrier and associated failures (precursors)
WP 3.3 (Dec2013)
Elaboration of an accident scenario modeling tool
WP 3.5 (June 2014)
Method for in service events analysis to identify safety barrier failures, issue recommendations and design requirements for current and future developments
CATS, FAST inputs
ATM NEMMO tool input
CAST, EASP inputs
WP3 Safety
Risk Assessment
WP4 Certification Case Studies
DRAFT

## Slide 65
WP3.1 Total Aviation Safety Assessment Methodology
Back up slides
DRAFT

## Slide 66: Total Aviation Safety Assessment Methodology (1/6)
QUESTIONS AND ANSWERS
Methodology objectives
Provide existing organisations, industry, operators and authorities with means to improve the safety level. Identification of gaps and shortcomings, coherence between certification and Safety Assurance and propose actions to improve: “evolution, not revolution”. Would you agree !
DRAFT

## Slide 67: Total Aviation Safety Assessment Methodology Q & A (2/6)
Necessary harmonization between aviation systems has to select a core of methods
Short listed methods, candidate for ASCOS Safety enhancement are
CATS with ESD, FT, BBN is an integrator of several principles
Functional Hazard Assessment (FHA)
Preliminary System Safety Assessment (PSSA)
System Safety Assessment (SSA)
Fault Tree Analysis
Dependence Diagram/Markov Analysis
Failure Modes and Effects Analysis (FMEA)
Failure Modes and Effects Summary (FMES)
Common Cause Analysis (CCA)
Zonal Safety Analysis (ZSA)
Particular Risks Analysis (PRA)
Common Mode Analysis (CMA)
Specific detailed standards do not need to be common (e.g. Approach procedures protection surfaces ≠ engines uncontained events )
Are You OK ?
QUESTIONS AND ANSWERS
DRAFT

## Slide 68: Total Aviation Safety Assessment Methodology Q & A (3/6)
QUESTIONS AND ANSWERS
FAST a self standing safety process ?
No, it’s not; it’s a means to augment most existing processes that provides:
Risks pictures of the future made available in all program phases to any safety and engineering and program actor in all aviation systems and interfaces.
More efficient search for precursors. FAST identifies areas where possible changes can generate new risks and contributes to define how detecting precursors (minor incidents, weakening safety barriers etc : ref section 3) of emerging and future risks.
It is part of evolution not revolution
It provides information available to all management actors including engineering and management.
Is it clear ?
DRAFT

## Slide 69: Total Aviation Safety Assessment Methodology Q & A (4/6)
QUESTIONS AND ANSWERS
There’s nothing new in ASCOS, we already do that
Aviation has already achieved a very good safety level with existing practices. It was necessary to list them before proposing improvements. The study revealed that improvements depend on the elimination of gaps and shortcomings in processes and on more anticipation in all program activities.
Anticipation is brought by FAST and resulting future risks scenarios and contribution to precursor’s detection.
Fighting against gaps is a management issue. More precisely a tighter Program / Engineering / Safety management issue therefore a top level management matter.
Comments ?
DRAFT

## Slide 70: Total Aviation Safety Assessment Methodology Q & A (5/6)
QUESTIONS AND ANSWERS
Process for identification of precursors for future and emerging risks – Questions:
  Methods => Data-driven, model based approaches, expert opinion
  Precursors in development phases
  Engineering support to operations
  Certification considerations
  Organization issues
  Legal feasibility  ref detailed comments
DRAFT